## Slide 1: CAZZAX1-based model Inverse kinematics
Simone Vollaro

## Slide 2: Project overview
First founded in 2016, the Finland-based company Cazza devised a concept for an industrial 3D printer using concrete to construct buildings up to two floors high.
After receiving attention and funds from a variety of backers thanks to their promises in terms of printing speed and material consumption, one of the cofounders stole all of the company budget and disappeared.
Since there is not even a prototype of the machine, nor prototyping documentation, the following is a model simulation based on the visual concepts and available information of the 3D printing arm: the Cazza X1.
Notes: 100mm per second
19-year-old Chris Kelsey
Drone: Obliterate, 3D Print, Lift & Place

## Slide 3: Arm concept
For this redundant manipulator we designed a model having 12 joints:
4 prismatic joints
8 rotoidals joints

## Slide 4: Model design
L1
L2
L3
L4
L5
L8
L6
L7
L9
L12
L10 - L11
J1
J2
J3
J4
J5
J8
J6
J7
J9
EE
J10 - J11 – J12
Joints J1, J2, J3 are considered being of the same part of the robot: the moving base.
Similarly, joints J10, J11, J12 are all part of the spherical wrist.

## Slide 5: Reference systems
y0
x0
z0
x1
z1
y1
z2
y2
x2
y3
x3
z3
x4
z4
y4
y5
x5
z6
y6
x6
y8
x8
z7
z8
y7
x7
y10
y9
x9
z10
z9
z11
y11
x11
x10
x12
z12
y12
z5
d1
d2
d4
θ5
θ3
θ6
θ7
θ8
d9
θ10
θ11
θ12
05 ≡ 04
07 ≡ 08
09 ≡ 010 ≡ 011

## Slide 6: Denavit - Hartenberg
Ref. systems | Link | a | α | d | θ
{S0} → {S1} | L0 | 0 | π/2 | d1 | π/2
{S1} → {S2} | L1 | 0 | π/2 | d2 | π/2
{S2} → {S3} | L2 | 0 | 0 | d3 | π/2 + θ3
{S3} → {S4} | L3 | 0 | 0 | d4 | -π/2
{S4} → {S5} | L4 | 0 | π/2 | 0 | θ5
{S5} → {S6} | L5 | a6 | 0 | 0 | θ6
{S6} → {S7} | L6 | a7 | 0 | 0 | θ7
{S7} → {S8} | L7 | 0 | π/2 | 0 | π/2 + θ8
{S8} → {S9} | L8 | 0 | -π/2 | d9 | 0
{S9} → {S10} | L9 | 0 | -π/2 | 0 | -π/2 + θ10
{S10} → {S11} | L10 | 0 | -π/2 | 0 | π/2 + θ11
{S11} → {S12} | L11 | a12 | 0 | 0 | π/2 + θ12

## Slide 7: Tasks description
As a main task, the end-effector has to move along a square trajectory, resembling the four walls of a simple kind of building.
Additionally, the base of the manipulator has to move around the building on a circular path.
For both the tasks, we devised a constant reference system on which the manipulator would have to orientate itself
Desired tasks can be accustomed to target kind of building and subdivided in more steps as needed.

## Slide 8: CLIK algorithm with task priority strategy
where
matrix needed to use the geometrical Jacobina instead of the analytical Jacobian; nd , n, sd , s, ad , a are respectively the normal, sliding, approach versors of the desired trajectory and the actual orientation.
twist of the desired part of the robot, comprising of the correction due to the position and orientation error
projector in the nullspace of the Jacobian matrix
subscripts “e” and “2” refers respectively to the first task (end effector positioning) and second task (robot base movements)
modification of the Jacobian for the second task, due to the task priority approach

## Slide 9: Resulting simulation

## Slide 10: RESULTING CONFIGURATION VARIABLES

## Slide 11: POSITION AND ORIENTATION ERRORS
PTP
Side1
Side2
Side3
Side4

## Slide 12: References
The overall project makes extensive use of content based on the following:
Lecture notes from Marco Gabiccini’s Master Course in Robot Mechanics (Robotics and Automation Engineering master degree)
B. Siciliano, L. Sciavicco, L. Villani, G. Oriolo, “Robotics: Modelling, Planning and Control"
Stefano Chiaverini, “Singularity-Robust Task-Priority Redundancy Resolution for Real-Time Kinematic Control of Robot Manipulators”
Pasquale Chiaccio, Bruno Siciliano, “Closed-Loop Inverse Kinematics Schemes for Constrained Redundant Manipulators with Task Space Augmentation and Task Priority Strategy”
Ashish Singla, Prasad Kulkarniy, Sandeep Kumary, Bhaskar Dasgupta , “Redundancy Control of Robot Manipulators using Task Priority”
Images taken from:
fabbloo.com
Fanatical Futurist Youtube channel
3ders.org (website now expired)